# W. W. Hansen Experimental Physics Laboratory

# STANFORD UNIVERSITY

# STANFORD, CALIFORNIA  94305  -  4085

# Gravity Probe B Relativity Mission

Detailed Specification

Gas Management Assembly

S0569 Rev A

May 20, 2002

| Approved by: Jeff Vanden Beukel Date Space Vehicle Product Team Manager | Approved by: Chris Gray Date GMA Responsible Engineer |
| --- | --- |
| Approved by: Ken Bower Date GMA Engineer | Approved by: Rob Brumley Date Technical Payload Manager |
| Approved by: Barry Muhlfelder Date Program Technical Manager | Approved by: Tom Langenstein Date Deputy Program Manager |
| Approved by: Dorrene Ross Date SU Quality Assurance | Approved by: Sasha Buchman Date Program Manager |
| __________________________________________ Approved by: Rich Whelan Date Systems Engineering |  |

ITAR Assessment Performed ITAR Control Req’d? Yes No Tom Langenstein

DOCUMENT REVISION RECORD

Document Title: Detailed Specification Gas Management Assembly for the Gravity Probe-B Space Vehicle

Document Number: S0569 Rev A

Dated: May 20,  2002

Rev. -	Authorization  Paragraph		Change Description

for Change

|  |  | 2.1 | Add Moog Workmanship Standard for Soldering. Moog follows NASA-STD-8739.3 |
| --- | --- | --- | --- |
|  |  | 2.1 | Add Moog Standard for Crimping. Moog follows Moog EP 3609 |
|  |  | 3.1.3.3 | Changed wording: From 5000( minimum to 5000( +/- 20% Table 1:Removed full scale max. voltage requirement; added ECU gain, Sensor F/S, and Max. expected pressure |
|  |  | 3.2.1.2 | Change from Flow Rate Volume to Flow Rate Mass (SCCM to mg/Sec) |
|  |  | 3.2.1.3 | Change from Flow Rate Volume to Flow Rate Mass (SCCM to mg/Sec) and changed tolerance from (10% to 50% |
|  |  | 3.2.1.4 | Change from Flow Rate Volume to Flow Rate Mass (SCCM to mg/Sec) and changed tolerance from 10% to 50%. Increased maximum flow from (10 sccm to .0364 mg/sec. |
|  |  | 3.2.1.5 | Change from Flow Rate Volume to Flow Rate Mass (SCCM to mg/Sec) and added +/-20% tolerance |
|  |  | 3.2.1.7 | Add note defining the pressure measurement location (Changed wording: Removed pressure requirement; defined purpose of requirement is to meet gas purity through-out the assembly) |
|  |  | 3.2.2.3.5 | Revised limit loads: was TBD |
|  |  | 3.2.2.7 | Added note stating acceptable method for verification |
|  |  | 3.2.2.8 | Defined the leakage rate requirement within the GMA temperature operating range |
|  |  | 3.2.2.8.1 | Defined the leakage rate requirement for the GMA at survivability temperatures |
|  |  | 3.2.5.1.2 | Revised Random Vibration Spectrum from 11.0 to 11.1 Grms |
|  |  | 3.2.8.1 | Add wording: from 99.9995% and 99.9990% purity to 99.9995% and 99.9990% or better purity |
|  |  | 3.2.8.2 | Add wording: from 99.9995% purity to 99.9995% or better purity |
|  |  | 3.3.1.6 | Changed wording: From bare metal to Resistance < 1 ohm. Removed wording “GMA to spacecraft” |
|  |  | 3.3.1.1 | Added a note stating an acceptable method for verification of non-compliance PMP's |
|  |  | 3.3.2 | Removed wording: NASA NHB 5300.4 (3A-1), 5300.4 (3G), 5300.4 (3H) NASA-STD-8739.3 Added wording: Moog EP 3609 and requirement 69 to Mil-STD-454 |
|  |  | 4.2.2.1 | Removed wording: from test sequence to Tests in title, removed "sequence" in description, and removed test sequence numbering.- Note: Sequence covered in ATP. |
|  |  | 4.2.2.2.6 | Changed wording: from "each" to "all" for better clarification |
|  |  | 4.2.3.2.3 | Revised number of thermal cycles to 3 |

Document Number: S0569 Rev -

Dated:  August 20, 2001

Rev. -		Authorization		Paragraph		Change Description

for Change

TABLE OF CONTENTS

1. Scope	1

1.1 General	1

1.2 Function	1

2. APPLICABLE DOCUMENTS	1

2.1 Government Documents	1

2.2 Non-Government Documents	1

3.0 REQUIREMENTS	2

3.1 Interfaces	2

3.1.1 Functional Interface	2

3.1.2 Mechanical Attachments	2

3.1.3 Electrical Interface	2

3.1.3.1 Valves	2

3.1.3.2 Temperature Sensors	2

3.1.3.3 Pressure Transducers	2

3.2 Characteristics	3

3.2.1 Performance	3

3.2.1.1 Gas Supply	3

3.2.1.2 Mass Flow Rate – Gyro Spin Up	3

3.2.1.3 Mass Flow Rate – Gyro Slow Spin	3

3.2.1.4 Mass Flow Rate – Exchange Gas	4

3.2.1.5 Mass Flow Rate – System Purge	4

3.2.1.6 Pressure Transducer Accuracy	4

3.2.2 Physical Characteristics	4

3.2.2.1 Mass	4

3.2.2.2 Space Envelope	4

3.2.2.3 Structural Integrity	4

3.2.2.3.1 Proof Pressure	4

3.2.2.3.2 Burst Pressure	4

3.2.2.3.3 Collapse Pressure	5

3.2.2.3.4 Pressure Vessel Safety	5

3.2.2.3.5 Limit Inlet Load	5

3.2.2.3.6 Strength	5

3.2.2.4 Redundancy	6

3.2.2.5 Electrical Characteristics	6

3.2.2.5.1 Electrical Circuits	6

3.2.2.5.2 Wire Harnessing	6

3.2.2.5.3 Conductors	6

3.2.2.5.4 Insulation Resistance	6

3.2.2.5.5 Wire Damage	6

3.2.2.7 External Leakage	6

3.2.2.8 Internal Leakage	6

3.2.2.8.1 Internal Leakage (Survival)				      5

3.2.2.9 Contamination	6

3.2.2.9.1 Internal Contamination	6

3.2.2.9.2 External Contamination	7

3.2.2.9.3 Self-Generated Contaminants	7

3.2.2.9.4 Purging Capability	7

3.2.2.10 Cycle Life Margin	7

3.2.3 Reliability	7

3.2.4 Maintainability	7

3.2.5 Environmental Conditions	7

3.2.5.1 Non-Operating Environments	7

3.2.5.1.1 Transportation, Handling and Storage Environment	7

3.2.5.1.2 Launch and Ascent Environment	7

3.2.5.1.3 Pyroshock	7

3.2.5.2 Operating Environments	9

3.2.5.2.1 Temperature	9

3.2.5.2.2 Acceleration and Sustained Load	9

3.2.5.2.3 Solar Radiation	9

3.2.6 Transportability	10

3.2.7 Useful Life	10

3.2.7.1 Shelf Life	10

3.2.7.2 Operating Life	10

3.2.7.2.1 Orbital Life	10

3.2.7.2.2 Cycle Life	10

3.2.8 Operating Conditions	10

3.2.8.1 Pressurant Fluids	10

3.2.8.2 Test and Cleaning	10

3.3 Design and Construction	10

3.3.1 Parts, Materials and Processes	10

3.3.1.1 Outgassing	11

3.3.1.2 Dissimilar Metals	11

3.3.1.3 Corrosion Resistance	11

3.3.1.4 Fungus Resistance	11

3.3.1.5 Electronic Equipment	11

3.3.1.6 Bonding and Grounding	11

3.3.1.7 Contamination Control	11

3.3.1.8 Lubricants	11

3.3.2 Workmanship	11

3.3.3 Product Marking	12

4. QUALITY ASSURANCE PROVISIONS	13

4.1 General	13

4.1.1. Responsibility for Tests	13

4.2 Quality Conformance Inspections	13

4.2.1 General Test Conditions	13

4.2.1.1 Ambient Conditions	13

4.2.1.2 Calibration	13

4.2.1.3 Test Sequence	13

4.2.1.4 Performance Checks	13

4.2.2 Acceptance Tests	14

4.2.2.1 Test Sequence	14

4.2.2.2 Test Methods	14

4.2.2.2.3 Proof Pressure	14

4.2.2.2.4 External Leakage	14

4.2.2.2.5 Ambient Functional	14

4.2.2.2.6 Cleanliness and Gas Purity Verification	14

4.2.2.2.7 Mass Properties	15

4.2.3 Protoqualification Tests	15

4.2.3.1 Test Sequence	15

4.2.3.2 Test Methods	15

4.2.3.2.1 Random Vibration	15

4.2.3.2.2 Abbreviated Ambient Functional	15

4.2.3.2.3 Thermal Cycling	16

4.2.3.2.4 Hot/Cold Leakage	17

4.2.3.2.5 Hot/Cold Functional	17

4.3 Verification	17

4.3.1 General	17

4.3.2 Responsibility for Verification	18

4.3.3 Verification Methods	18

4.3.3.1 Similarity	18

4.3.3.2 Analysis	18

4.3.3.3 Inspection	18

4.3.3.4 Demonstration	18

4.3.3.5 Tests	18

5. PREPARATION FOR DELIVERY	23

5.1 Packing	23

# 1. scope

## 1.1 General

This specification establishes the performance and test requirements for the Gravity Probe-B Gas Management Assembly, hereinafter referred to as the GMA.

## 1.2 Function

The GMA provides helium gas at specified flow rates for use in spinning-up gyroscopes, and as exchange gas in the Probe.

# 2. APPLICABLE DOCUMENTS

## 2.1 Government Documents

The following government documents are applicable to the extent specified in this document.  In the event of conflict between the documents referenced herein and the contents of this specification, the contents of this specification supersede.

MIL-STD-454		Standard General Requirements for Electronic Equipment (tailored)

MIL-STD-975		NASA Standard Electrical, Electronic and Electromechanical (EEE) Parts List

MIL-STD-1522A	Standard General Requirements for Safe Design and Operation of Pressurized Missile and Space Systems

MIL-HDBK-5		Metallic Materials and Elements for Aerospace Structures

NHB 5300.4 (3A-1)	Workmanship Standard for Soldering

or NASA-STD-8739.3

Moog EP 3609	Workmanship Standard for Crimping

## 2.2 Non-Government Documents

The following documents are applicable to the extent specified in this document.  In the event of conflict between the documents referenced herein and the contents of this specification, the contents of this specification supersede.

8A02681		GMA Interface Control Drawing

# 3.0 REQUIREMENTS

## 3.1 Interfaces

### 3.1.1 Functional Interface

The input/output functions are shown in Figure 1.

Fig. 1 Functional Interfaces

### 3.1.2 Mechanical Attachments

The interfacing mounting surface, attach points, electrical connectors, keep-out zones, and gas inlets and outlets will be compatible with the configurations and locations shown in LM drawing 8A02681.

### 3.1.3 Electrical Interface

The interfacing electrical circuits will be wired as shown in LMMS drawing 8A02681.

#### 3.1.3.1 Valves

The valves shall be supplied a 30 V input, which is provided to the Latch Valve through a circuit which has a 4 ohm resistor in series. The pulse duration is 450 msec plus/minus 10 %.  The resistance of each valve coil will be 58 ± 1 ohms at 70 ± 5 °F.

#### 3.1.3.2 Temperature Sensors

Silicon Diode Temperature sensors will be supplied to the vendor as GFE.

#### 3.1.3.3 Pressure Transducers

The pressure transducers shall be supplied with an excitation voltage of 10 ± .5 Volts.  The input resistance shall be 5000 ohms +/- 20%. The transducer resolution, full scale, and expected maximum pressures are shown in Table 1.

| ID # | ECU Side | Gain | Pressure Sensor Full Scale (psia) | GMA Max. Expected Pressure(psia) |
| --- | --- | --- | --- | --- |
| GP2 | A | 330 | 2500 | 2000 |
| GP10 | A | 1300 | 15 | 15 |
| GP1 | A | 300 | 2500 | 2000 |
| GP7 | A | 1000 | 15 | 15 |
| GP11 | A | 1000 | 15 | 15 |
| GP13 | A | 500 | 15 | 15 |
| GP4 | A | 500 | 50 | 25 |
| GP8 | B | 1300 | 15 | 15 |
| GP14 | B | 1300 | 15 | 15 |
| GP9 | B | 1000 | 15 | 15 |
| GP12 | B | 1000 | 15 | 15 |
| GP6 | B | 1000 | 50 | 25 |
| GP3 | B | 500 | 5000 | 2000 |
| GP5 | B | 500 | 50 | 25 |

Table 1. Transducer Resolution

## 3.2 Characteristics

### 3.2.1 Performance

The GMA shall have the following performance upon command at the operating conditions

specified in 3.2.8 and environments specified in 3.2.5 throughout the life specified in 3.2.7.

#### 3.2.1.1 Gas Supply

The GMA shall be capable of providing a minimum of 1100 liters of Helium gas [Standard Temperature and Pressure (0 deg C, 760 torr)] at the outlets of the GMA, while maintaining a minimum tank pressure of 689,500 Pa (100 psia).

#### 3.2.1.2 Mass Flow Rate – Gyro Spin Up

The GMA shall be capable of providing helium gas at a mass flow rate of 2.2 mg/sec (± 20% @21( C), calculated using Root Sum Squared (RSS), to each of the Science Gyroscopes.  This flow rate is only required for one gyro at a time and assumes the downstream inlet pressure for each gyroscope inlet at the Probe is 40 Torr.

#### 3.2.1.3 Mass Flow Rate – Gyro Slow Spin

The GMA shall be capable of providing helium gas at a mass flow rate of 0.006 mg/sec (± 50 % @21( C), calculated using Root Sum Squared (RSS), to each of the Science Gyroscopes. This flow rate is only required for one gyro at a time and assumes the downstream inlet pressure for each gyroscope inlet at the Probe is 40 Torr.

#### 3.2.1.4 Mass Flow Rate – Exchange Gas

The GMA shall be capable of providing helium gas at a mass flow rate of 0.006 mg/sec (± 50 % @21( C), calculated using Root Sum Squared (RSS), at the inlet to the probe. This flow rate assumes the downstream inlet pressure at the probe is < 1 X10 – 8 torr. The design shall incorporate features in the event of failure to incorporate a maximum flow of 0.0364mg/sec into the probe.

#### 3.2.1.5 Mass Flow Rate – System Purge

The GMA shall be capable of purging helium gas at a mass flow rate of 2.2 mg/sec (± 20% @21( C), calculated using Root Sum Squared (RSS), through the non-propulsive vent outlet.

#### 3.2.1.6 Pressure Transducer Accuracy

The output produced by the pressure transducers shall be within 1.5% of full-scale value of the value predicted by the calibration curve for a given unit.  This accuracy is required over the range of survival temperatures specified in, and during and after exposure to a total radiation dose of 50Krads.

3.2.1.7 Evacuation

The GMA system shall be capable of an internal vacuum sufficient to meet gas purity requirements.

Note: The pressure is to be measured at the gas inlet port, (Fill and Drain) while the GMA is being evacuated at the outlet ports.

### 3.2.2 Physical Characteristics

The GMA shall have the following physical characteristics before, during (where applicable) and after exposure to the environments specified in 3.2.5.

#### 3.2.2.1 Mass

The assembled GMA mass shall be less than 64 kg.

#### 3.2.2.2 Space Envelope

The GMA external dimensions shall meet the space envelope requirements shown in LM drawing 8A02681.

#### 3.2.2.3 Structural Integrity

The GMA shall be capable of withstanding the following loads:

##### 3.2.2.3.1 Proof Pressure

The system proof pressure shall be 1.5 times Maximum Expected Operating Pressure (MEOP).

##### 3.2.2.3.2 Burst Pressure

The system design burst pressure shall be 2 times Maximum Expected Operating Pressure (MEOP) for tanks, 4.0 times for tubing and fittings, and 2.5 times MEOP for other components.  Successful operation of system components is not required after exposure to burst pressure.

##### 3.2.2.3.3 Collapse Pressure

The GMA shall withstand a collapse pressure of 101,325 Pa-differential (14.7 psid).

##### 3.2.2.3.4 Pressure Vessel Safety

The GMA tanks and components shall meet the requirements of MIL-STD-1522A.  The tanks shall be designated “Fracture Critical” and handled appropriately. Vendor shall supply "Fracture Control" plan.

##### 3.2.2.3.5 Limit Inlet Load  The limit loads for the Gamah fitting brackets shall be derived from the secondary structures load curve, (SSD Structural Design Criteria, LMSC/D887697). For simplicity, normal and in-plane accelerations shall be combined and applied at each axis to produce the following loads. See figure 2.

The Gamah fitting bracket shall be designed to resist the following loads.

# Px	=	50 lbf

Py	=	50 lbf

Pz	=	50 lbf

Figure 2 Gamah Fitting Bracket (free-body)

##### 3.2.2.3.6 Strength

The GMA shall withstand the stress resulting from the loads specified in 3.2.2.3.5 with positive margins of safety using factors of safety of 1.25 for yield and 2.0 for ultimate.

3.2.2.3.7 First Structure Mode

Natural frequency of assembled GMA shall be greater than 50 Hz.

#### 3.2.2.4 Redundancy

Redundancy shall be provided to ensure that, to the greatest extent practicable, there are no single point failures.

#### 3.2.2.5 Electrical Characteristics

The electrical components of the GMA shall have the following characteristics:

##### 3.2.2.5.1 Electrical Circuits

To the maximum extent practicable, primary failure conditions of input/output functions shall present electrically open circuits or very high impedance to interfacing equipment.

##### 3.2.2.5.2 Wire Harnessing

All conductor sizes shall be adequate for the expected current and voltage levels.

##### 3.2.2.5.3 Conductors

All conductors shall be twisted shielded pair type.

##### 3.2.2.5.4 Insulation Resistance

The insulation resistance between all electrically isolated circuits, including unused pins, and the GMA ground plane shall not be less than 100 megaohms at 250 VDC.

##### 3.2.2.5.5 Wire Damage

Insulated hook-up and harness wire shall be protected from insulation damage due to abrasion, extrusion or other thermal or mechanical stress, which might expose conductors unintentionally.

#### 3.2.2.7 External Leakage

External gas leakage into the GMA shall be less than 1 x 10-6 (TBR-SU) scc/sec of Gaseous Helium with the interior evacuated. Note: An acceptable method for verifying this requirement is to pressurize the GMA to the launch configuration and measure the rate of helium leakage out of the system.

#### 3.2.2.8 Internal Leakage (Operational)

Internal leakage of each of the valves shall be less than 1 x 10-4 scc/sec of Gaseous Helium per seat at MEOP and at 20 psia inlet pressure through the GMA's operating temperature range (0-40C).

3.2.2.8.1 Internal Leakage (Survival)

System leakage at survival temperature (-49(C) shall be < 1.4 x 10-1scc/sec.

#### 3.2.2.9 Contamination

##### 3.2.2.9.1 Internal Contamination

Internal GMA components shall be cleaned to MIL-STD-1246 level 100A.  Assembly of the GMA shall occur in a clean room environment compatible with maintaining the specified level of cleanliness.

##### 3.2.2.9.2 External Contamination

GMA external surfaces shall be free of contamination when examined by an individual with 20/20 (or corrected to 20/20) vision under white light (min. 100-ft. candles), at an oblique angle, at a distance of 40 centimeters (16 inches).

##### 3.2.2.9.3 Self-Generated Contaminants

The GMA shall incorporate design features to minimize self-generated contaminants.

##### 3.2.2.9.4 Purging Capability

The GMA design shall maximize the ability to purge the GMA during ground and on orbit operations.

#### 3.2.2.10 Cycle Life Margin

After GMA protoqualification testing, all components shall have at least a 2 to 1 cycle life margin over the requirements specified in 3.2.7.2.2.

### 3.2.3 Failure Propagation

The GMA shall be designed so that a failure of a component will not induce any other failure external to the failed component.

### 3.2.4 Maintainability

The GMA design shall be such that scheduled maintenance and repair, or adjustments, are not required.

### 3.2.5 Environmental Conditions

The GMA shall perform as specified in 3.2.1 during exposure, if appropriate, and after exposure to all natural and induced environments experienced during the following: manufacture, test, transportation, handling, storage, launch-pad, ascent, and orbit operations.

#### 3.2.5.1 Non-Operating Environments

The GMA shall be designed to withstand, without degradation of the physical characteristics specified in 3.2.2, an atmospheric pressure from 95 to 108  103 Pa, a temperature of 16˚ to 35˚ C, and a relative humidity of not more than 90%. and the following non-operating requirements.

##### 3.2.5.1.1 Transportation, Handling and Storage Environment

The GMA, when packaged and packed in accordance with Section 5, shall not experience environmental conditions more severe than those specified for flight when the unit is exposed to the pre-flight transportation, storage and handling environments.

##### 3.2.5.1.2 Launch and Ascent Environment

The GMA shall be capable of withstanding the random vibration environment.  The protoqual random vibration environment shall be that shown in Figure 2.  The acceptance random vibration level is 3 dB lower than the protoqual level.

The Gas Management Assembly shall be capable of performance as specified herein after exposure to the random vibration environment as specified in Figure 3. The unit shall be subjected to an overall level of 11.1 Grms in each of 3 axes, 1 minute /axis. Test tolerance shall be as listed in Table 1.

Figure 3   GMA  Protoqual Random Vibration Environment

| PSD: | 20 to 1000 Hz: | +/-1.5dB |
| --- | --- | --- |
|  | 1000 to 2000 Hz: | +/-3dB |
| RMS: |  | ±10% overall |

Table 1 	Random Vibration Test Tolerance

3.2.5.1.3 Pyroshock

The GMA shall be capable of performing after exposure to the protoqual pyroshock environment shown in Figure 2.  Figure 2 is a Shock Response Spectrum with Q= 10.

The environment in Figure 4 applies to a test in the normal to mounting plane axis only.  The test tolerance is ±6 dB. With natural frequencies spaced at 1/6-octave intervals, at least 50 percent of the test spectrum values are greater than the nominal test specification.  The Off-axis (axes in-mounting-plane) test level (SRS) will be plotted with an overlay of the specified environment shown in Figure 4.

Figure 4.   GMA Interface Protoqual Pyroshock Environment

#### 3.2.5.2 Operating Environments

The GMA shall be designed to meet the performance requirements of 3.2.1 and the physical characteristic requirements of 3.2.2 in the following orbital environments.

##### 3.2.5.2.1 Temperature

|  | Operate | Survival |
| --- | --- | --- |
|  | Max | Min | Max | Min |
| Acceptance | 35C | 5C | 35C | -44C |
| Proto-qual | 40C | 0C | 40C | -49C |

##### 3.2.5.2.2 Acceleration and Sustained Load

The GMA design load is 15g to be applied in any direction.

##### 3.2.5.2.3 Solar Radiation

Not applicable, except for the solar radiation contribution to the thermal environment as defined in 3.2.5.2.

### 3.2.6 Transportability

The GMA, when packaged and packed in accordance with Section 5, shall be capable of being transported by air and road.

### 3.2.7 Useful Life

#### 3.2.7.1 Shelf Life

The GMA shall be designed to have a shelf/storage life of five years after protoqualification testing. The internal volume of the GMA shall be pressurized to a pressure not greater than 50 psig.

#### 3.2.7.2 Operating Life

##### 3.2.7.2.1 Orbital Life

The GMA will be capable of satisfactory operation in the orbital environment for a period of not less than 24 months.

##### 3.2.7.2.2 Cycle Life

Each latching valve shall be capable of 5,000 cycles after protoqualification test, at the maximum operating temperature specified in 3.2.5.2.1.  Each Fill/Drain valve shall be capable of 50 cycles after protoqualification, at ambient conditions.

### 3.2.8 Operating Conditions

#### 3.2.8.1 Pressurant Fluids

The GMA will be exposed to gaseous helium of 99.9995 % or better purity.  The gas supplied from the GMA shall be gaseous helium of 99.9990 % or better purity.

#### 3.2.8.2 Test and Cleaning

For testing purposes, gaseous Helium of 99.9995 % or better purity shall be used.  All cleaning fluids shall be compatible with the material of the GMA, and the specified cleanliness level.

## 3.3 Design and Construction

### 3.3.1 Parts, Materials and Processes

Parts, materials and processes shall be selected to meet the reliability requirements and environmental requirements specified herein.  The following materials are prohibited:

1) Cadmium, Zinc, or Selenium

2) Pure, unalloyed tin (greater than 99.1% tin)

3) Corrosive Solder Fluxes

4) Mercury and compounds of Mercury

5) Silicones which evolve a corrosive acid

#### 3.3.1.1 Outgassing

All materials exposed to vacuum shall not lose more than one (1) percent of total weight after exposure for 24 hours at 125 C and 1.333  10-4 Pa and no more than 0.1 percent of the material shall be in the form of vaporizable condensable materials.

Note: Gas wetted materials that do not meet this requirement shall be considered acceptable if gas purity analysis is acceptable.

#### 3.3.1.2 Dissimilar Metals

Where it is impractical to avoid dissimilar metals in direct contact with each other or their exposure to the same electrolyte, suitable protection shall be provided as required to meet the environmental requirements specified under paragraphs 3.2.5 herein.

#### 3.3.1.3 Corrosion Resistance

Metals shall either be of a corrosion resistant type or suitably treated or protected to resist corrosion.  Protective methods and materials for cleaning, surface treatment, and application of finishes and protective coatings shall be accomplished per contractor's best practices.  Cadmium, zinc, or electro-deposited tin shall not be used as a finish.

#### 3.3.1.4 Fungus Resistance

Materials that are nutrients for fungi shall not be used.

#### 3.3.1.5 Electronic Equipment

Electronic equipment shall be designed and manufactured in accordance with MIL-STD-454, Standard General Requirements for Electronic Equipment (tailored).  Reliability of parts shall meet the intent of class B (ICs), JANTXV (discrete semiconductors) and ERMIL (passive parts).

#### 3.3.1.6 Bonding and Grounding

The mounting surfaces for electrical connectors to the GMA shall be < 1.0 Ohms.

#### 3.3.1.7 Contamination Control

Procedures and processes shall be utilized to insure that contamination control limits are maintained on the unit during manufacture, assembly, test and transportation.  Whenever the internal flow passages of the GMA are exposed, the GMA shall be within a clean room level compatible with maintaining the specified level of cleanliness and gas purity.

#### 3.3.1.8 Lubricants

The GMA shall not use any lubricants in the wetted gas path.

3.3.1.9 Fasteners

Fasteners shall be NAS type with appropriate strength specifications.

### 3.3.2 Workmanship

The workmanship will be of quality to assure safety, proper operation, high reliability, and service life requirements. Particular attention will be given to neatness, cleanliness, and thoroughness of all processes involving assembly and finishing of all hardware items. Workmanship standards will be employed throughout all phases of hardware manufacture to control the quality of operation.  Electrical workmanship shall comply with Moog EP 3609 and MIL-STD-454 , Requirement 9 and Requirement 69 .

### 3.3.3 Product Marking

### The end-item GMA pallet shall be marked by engraving or other suitable method.

# 4. QUALITY ASSURANCE PROVISIONS

## 4.1 General

This section outlines quality assurance provisions necessary to verify the Section 3 performance/design characteristics and operability of the GMA.  The test program shall be in accordance with the specification herein.

### 4.1.1. Responsibility for Tests

Tests shall be performed by the GMA Vendor.

## 4.2 Quality Conformance Inspections

Formal qualification inspections, analyses and tests shall be conducted to validate that the GMA satisfies the requirements of Section 3 herein.  The GMA shall undergo acceptance testing and protoqualification testing.  This activity also shall verify the effectiveness of the manufacturing process. When environmental conditions cannot be properly or conservatively simulated in test, allowances for material properties, combined loading and other missing effects shall be provided in test procedures and applied loads.  Where prior loading histories affect the structural adequacy of a test article, these shall be included in all test requirements.  Adequate instrumentation shall be provided in order to evaluate test results.  All protoqualification testing shall be completed prior to the first flight.  Environmental acceptance testing shall be completed on the GMA prior to its installation on a flight or qualification model spacecraft.

### 4.2.1 General Test Conditions

#### 4.2.1.1 Ambient Conditions

Unless otherwise specified, the following tests shall be performed at an atmospheric pressure from 95 to 108  103 Pa, a temperature of 16˚ to 35˚ C, and a relative humidity of not more than 90%.  When tests are performed with atmospheric conditions substantially different from these values, proper allowance for changes in instrument readings shall be made to compensate for deviations from the specified conditions.

#### 4.2.1.2 Calibration

The accuracy of instruments and test equipment shall be periodically verified by the calibration procedures that ensure tracebility to NIST standards.

#### 4.2.1.3 Test Sequence

Operative and non-operative requirements may be verified during a single test sequence.

#### 4.2.1.4 Performance Checks

Prior to the conduct of each test, the test article shall be instrumented and checked for satisfactory performance under ambient room conditions.  Performance checks shall be made in accordance with the test procedures.  A record shall be made of all data necessary to determine complete operational and performance characteristics.

### 4.2.2 Acceptance Tests

#### 4.2.2.1 Required Test

The acceptance tests shall be as shown below:

Test				 Method

Dimensional Inspection		4.2.2.2.1

Insulation Resistance			4.2.2.2.2

Proof Pressure				4.2.2.2.3

External Leakage			4.2.2.2.4

Ambient Functional 			4.2.2.2.5

Cleanliness Verification		4.2.2.2.6

Mass Properties			4.2.2.2.7

#### 4.2.2.2 Test Methods

The methods of conducting tests shall be as follows:

4.2.2.2.1 Dimensional Inspection

Verify as-built dimensions and interface locations.

4.2.2.2.2 Insulation Resistance

Insulation resistance shall be verified using the method described in NHB 5300.4 (3G).

##### 4.2.2.2.3 Proof Pressure

Pressurize to 1.5 times MEOP.

##### 4.2.2.2.4 External Leakage

The GMA shall be evacuated using a helium leak detector.  All mechanical joints and 100 percent of the surface shall be checked using helium.

##### 4.2.2.2.5 Ambient Functional

The resistance of each valve coil shall be measured at ambient temperature.  The response of each latching valve shall be verified. The internal leakage rate of each latching valve shall be verified.  The regulation band of the pressure regulators shall be verified.  The calibration of each pressure transducer shall be verified.  The leakage rate of the fill/drain valves shall be verified.

With the GMA outlets exhausting into a pressure of 40 torr at the probe inlet, the helium mass flow output of each GMA flow path shall be verified at ambient temperature.  The flow output shall be verified at the Maximum and Minimum Expected Operating Pressures of the He supply tank system.

##### 4.2.2.2.6 Cleanliness and Gas Purity Verification

The outside surface of the GMA shall be visually examined to the criteria established in 3.2.2.9.2. Cleanliness and gas purity shall be demonstrated by collecting samples at all of the flow path outlets.

##### 4.2.2.2.7 Mass Properties

The mass of the GMA shall be measured and recorded.

### 4.2.3 Protoqualification Tests

#### 4.2.3.1 Required Tests

The protoqualification tests shall be as shown below:

Test				 Method

Acceptance Test			4.2.2.1

Random Vibration			4.2.3.2.1

Abbreviated Ambient Functional	4.2.3.2.2

External Leakage			4.2.2.2.4

Thermal Cycling			4.2.3.2.3

Hot/Cold Leakage			4.2.3.2.4

Hot/Cold Functional			4.2.3.2.5

Insulation Resistance			4.2.2.2.2

Ambient Functional			4.2.2.2.5

Cleanliness Verification		4.2.2.2.6

* The Hot/Cold Leakage and Functional Tests may be performed concurrently with the Thermal Cycling Test.

The pressure transducers shall be radiation tested separately.

#### 4.2.3.2 Test Methods

The methods of conducting tests shall be as follows:

##### 4.2.3.2.1 Random Vibration

The GMA shall be exposed to the protoqualification test random vibration environment as defined in paragraph 3.2.5.1.2.  The level shall be as shown in Figure 1.  The level shall be applied on each axis, one axis at a time.  The test tolerance shall be ±3 dB over the whole frequency range.  At the conclusion of testing, the GMA shall be visually examined for evidence of damage or adverse effects.

##### 4.2.3.2.2 Abbreviated Ambient Functional

The resistance of each valve coil shall be measured at ambient temperature.  The response of each latching valve shall be verified. The internal leakage rate of each plumbing branch shall be verified.  The regulation band of the pressure regulators shall be verified.  The calibration of each pressure transducer shall be verified.  The leakage rate of the fill/drain valves shall be verified.

##### 4.2.3.2.3 Thermal Cycling

The GMA shall be subjected to 3 thermal cycles between the minimum survival temperature specified in 3.2.5.2.1 and the maximum survival temperature in 3.2.5.2.1, while the GMA is in a vacuum of 1.33 Pa (10-2 torr) or lower.  Each temperature cycle shall begin at ambient temperature. The dwell time at the high and low temperature shall be 6 hours or greater during the first and last cycle.  Intermediate cycles shall have at least 1-hour soaks at the hot and cold temperatures with power turned on.  The temperature profile is shown in Figure 5.  The Hot/Cold Leakage (4.2.3.2.4) and Hot/Cold Functional Tests (4.2.3.2.5) shall be performed during the last thermal cycle.

Figure 5. Thermal Cycling Profile

##### 4.2.3.2.4 Hot/Cold Leakage

All mechanical joints and 100 percent of the GMA surface shall be checked using a helium leak detector at the minimum and maximum survival temperatures specified in 3.2.5.2.1.

##### 4.2.3.2.5 Hot/Cold Functional

The following tests shall be performed at the minimum and maximum operating temperatures.

The resistance of each valve coil shall be measured. The response of each latching valve shall be verified. The internal leakage rate of each latching valve shall be verified.  The regulation band of the pressure regulators shall be verified.  The calibration of each pressure transducer shall be verified.  The leakage rate of the fill/drain valves shall be verified. Performance of the thermal control components shall be verified.

With the GMA outlets exhausting into a pressure of 40 torr at the probe inlet, the helium mass flow output of each GMA flow path shall be verified the minimum and maximum operating temperatures.  The flow output shall be verified at the Maximum and Minimum Expected Operating Pressures of the He supply tank system.

## 4.3 Verification

### 4.3.1 General

The verification program shall ensure that the GMA conforms to the requirements specified in Sec 3. Each requirement will be verified as specified herein.

### 4.3.2 Responsibility for Verification

Verification that the GMA meets the design and performance requirements specified in Sec 3 is the responsibility of the Vendor.

### 4.3.3 Verification Methods

Qualification and acceptance shall be accomplished by any one or more of the following methods:

• Similarity

• Analysis

• Inspection

• Demonstration

• Test

#### 4.3.3.1 Similarity

Verification by similarity is the process of assessing by review of prior test data or hardware configuration and application that the article is similar or identical in design and manufacturing process to another article that has previously been qualified to equivalent or more stringent specifications.

#### 4.3.3.2 Analysis

Verification by analysis is a process used in lieu of or in addition to testing to verify compliance to specification requirements. The selected techniques may include systems engineering analysis, statistics and qualitative analysis, computer and hardware simulations, and analog modeling. Analysis may be used when it can be determined that:

•	Accurate analysis is possible

•	Test is not cost-effective or physically possible

•	Similarity is not applicable

•	Verification by inspection is not adequate.

#### 4.3.3.3 Inspection

Verification by inspection (that is, physical verification of compliance with drawings, wire coding, material compliance) may be used in lieu of or in conjunction with testing to verify design features.

#### 4.3.3.4 Demonstration

Validation by demonstration is the process where demonstration techniques (for example, service access, transportability, crew-hardware interfaces, and replacement provisions) are used in lieu of or in conjunction with test to verify compliance with the requirements.

#### 4.3.3.5 Tests

Verification tests may be functional or environmental. Functional testing is conducted on flight or flight-configured hardware at conditions equal to or less than design specifications. Its purpose is to establish that the hardware performs satisfactorily in accordance with design specifications. Environmental testing is conducted on flight or flight-configured hardware to ensure the flight hardware will perform satisfactorily in its flight environment. Examples are vibration, acoustic, and thermal-vacuum. Environmental testing may or may not be combined with functional testing, depending on the objectives of the test.

4.3.4 Verification Selection

The methods selected for verification of the design and performance requirements of Sec 3 are presented in the verification matrix, Table 4.3-1.

3.1 	Interfaces 		N/A

3.1.1 	Functional Interface					X

3.1.2 	Mechanical Attachments			X

3.1.3 	Electrical Interface					X

3.1.3.1 	Valves					X

3.1.3.2	Temperature Sensors						N/A

3.1.3.3 	Pressure Transducers					X

3.2 	Characteristics						N/A

3.2.1 	Performance						N/A

3.2.1.1	Gas Supply					X

3.2.1.2	Mass Flow Rate – Gyro Spin Up					X

3.2.1.3	Mass Flow Rate – Gyro Slow Spin					X

3.2.1.4	Mass Flow Rate – Exchange Gas					X

3.2.1.5	Mass Flow Rate – System Purge					X

3.2.1.6	Pressure Transducer Accuracy					X

3.2.2 	Physical Characteristics						N/A

3.2.2.1 	Mass					X

3.2.2.2 	Space Envelope			X

3.2.2.3 	Structural Integrity						N/A

3.2.2.3.1 	Proof Pressure					X

3.2.2.3.2 	Burst Pressure					X

3.2.2.3.3 	Collapse Pressure					X

3.2.2.3.4 	Pressure Vessel Safety		X			X

3.2.2.3.5	Limit Inlet Load		X

3.2.2.3.6	Strength		X

3.2.2.4	Redundancy		X

3.2.2.5	Electrical Characteristics						N/A

3.2.2.5.1	Electrical Circuits		X

3.2.2.5.2	Wire Harnessing		X	X

3.2.2.5.3	Conductors			X

3.2.2.5.4	Insulation Resistance					X

3.2.2.5.5	Wire Damage			X

3.2.2.7	External Leakage					X

3.2.2.8 	Internal Leakage					X

3.2.2.8.1	Internal Leakage (Survival)	X				X

3.2.2.9 	Contamination						N/A

3.2.2.9.1 	Internal Contamination			X

3.2.2.9.2 	External Contamination			X

3.2.2.9.3 	Self-Generated Contaminants		X			X

3.2.2.9.4	Purging Capability		X

3.2.2.10 	Cycle Life Margin	X

3.2.3 	Reliability		X

3.2.4 	Maintainability		X

3.2.5 	Environmental Conditions						N/A

3.2.5.1 	Non-Operating Environments						N/A

3.2.5.1.1 	Transportation, Handling and

Storage Environment		X

3.2.5.1.2 	Launch and Ascent Environment		X			X

3.2.5.1.3 	Pyroshock					X

3.2.5.2 	Operating Environments						N/A

3.2.5.2.1 	Temperature					X

3.2.5.2.2 	Acceleration and Sustained Load		X

3.2.5.2.3	Solar Radiation						N/A

3.2.6 	Transportability		X

3.2.7 	Useful Life

3.2.7.1 	Shelf Life		X

3.2.7.2 	Operating Life						N/A

3.2.7.2.1 	Orbital Life	X

3.2.7.2.2 	Cycle Life	X

3.2.8 	Operating Conditions						N/A

3.2.8.1 	Pressurant Fluids			X

3.2.8.2 	Test & Cleaning			X

3.3 	Design and Construction						N/A

3.3.1 	Parts, Materials and Processes			X

3.3.1.1 	Outgassing		X

3.3.1.2 	Dissimilar Metals			X

3.3.1.3 	Corrosion Resistance			X

3.3.1.4 	Fungus Resistance			X

3.3.1.5 	Electronic Equipment			X

3.3.1.6 	Bonding and Grounding			X

3.3.1.7 	Contamination Control			X

3.3.1.8	Lubricants			X

3.3.2	Workmanship			X

3.3.3 	Nameplates and Product Marking			X

# 5. PREPARATION FOR DELIVERY

## 5.1 Packing

The GMA shall be packaged to maintain the contamination level specified in 3.2.2.9.  The GMA shall be packed separately in a container that includes a shock and vibration mitigation system capable of protecting each item as required by 3.2.5.1.1.  The vibration and shock mitigation system shall secure each item to prevent movement during transportation and handling.  Individual containers shall be so constructed as to allow removal of parts for inspection without damage to the container or labels.