W. W. Hansen Experimental Physics Laboratory

STANFORD UNIVERSITY

STANFORD, CALIFORNIA  94305  -  4085

Gravity Probe B Relativity Mission

Dewar Lifetime & TAO Assessment

following Thermal Vacuum Test 2

S0917, Rev. -

August 15, 2003

| Prepared by: John Mester Date |  |
| --- | --- |
| Approved by: Rob Brumley Date |  |
| Approved by: Systems Engineering Date | Approved by: Quality Assurance Date |

ITAR Assessment Performed ITAR Control Req’d? Yes No Tom Langenstein

Purpose:

This document formally releases the presentation material prepared for the June 12, 2003 review of the Thermal Vacuum Test #2.

The attached charts show that the Dewar predicted on-orbit lifetime is 18.8 months, and that this value is supported by a host of test and analytical data.

Additionally, the effect known as Thermal Amplitude Oscillation (TAO) has been shown to be a ground concern only, and will not occur on orbit.

For U. S. Export control reasons, pages which show the Lockheed Martin thermal model details have been omitted.